## Slide 1
TUNING PID CONTROLLERS USING TD3-RL FOR NONLINEAR SYSTEMS
IE415: CONTROL OF AUTONOMOUS SYSTEMS
Name: Jeet Patel
ID: 202201216
Prof. Sujay Kadam

## Slide 2
MOTIVATION
FOR CHOOSING THIS TOPIC

## Slide 3
INTRODUCTION
  Brief overview of PID controllers and their significance in control systems.
    Proportional: Responds to current error.
    Integral: Addresses accumulated error over time.
    Derivative: Predicts and compensates for future error changes.
  Challenges in tuning PID for nonlinear systems.
    Nonlinearity
    Dynamic Changes
    Manual Tuning
  Motivation for using Reinforcement Learning (RL) and TD3 algorithm
    Adaptability
    Optimal Control
    Automation

## Slide 4
OBJECTIVE
  Compare RL-based tuning with conventional PID tuning.
  Apply the TD3 algorithm to train a PID controller for a mass-spring-damper system.
  Simulate and evaluate the performance of RL-tuned PID controllers.

## Slide 5
SYSTEM DESCRIPTION
mx” + cx’ + kx = F
  Behavior:
    Spring: Resists displacement proportionally (kx).
    Damper: Opposes velocity (cx’) for stability.
    Mass: Reacts to applied forces with acceleration (mx”).
  Purpose:
    Models real-world systems like car suspensions or robotic joints.
    Used to analyze dynamic responses to various inputs (e.g., step, sinusoidal).
  Control Objective:
    Achieve stable performance with minimal overshoot and fast settling by controlling the force F.

## Slide 6
REINFORCEMENT LEARNING OVERVIEW

## Slide 7
  Agent:
    The decision-maker that learns to optimize control by interacting with the environment.
  Environment:
    The system or process the agent interacts with (e.g., mass-spring-damper system).
  Policy:
    Probability of selecting a possible action given a state and reward.
  State:
    A representation of the system's current condition (e.g., position, velocity).
  Action:
    The control input applied by the agent to influence the environment (e.g., force).
  Reward:
    Feedback signal guiding the agent's learning, based on the desirability of its actions.
RL CONCEPTS

## Slide 8
TD3 ALGORITHM
Twin Delayed Deep Deterministic Policy Gradient
  DDPG shortcomings: i. Overestimation bias
ii. Numerical instability
  Replay Buffer
  To reduce Overestimation bias in: DDPG TD3 uses three techniques
  Clipped double Q-learning
  Target policy smoothing
  Delayed policy and target updates

## Slide 9
SIMULATION SETUP
  Simulink model components:
    Observation block: Outputs P, I, D.
    Reward block: Implements the designed reward function.
    RL Agent: Uses TD3 to adjust KP, KI, KD.
  Training parameters:
    Episodes: 500
    Mini-batch size: 128
    Discount factor: 0.97
    Learning rates for actor and critic.

## Slide 10
REWARD FUNCTION DESIGN
  Reward components:
    Penalty for overshooting: −2000.
    Penalty for weak control: -100
    Reward for staying within target: +3.
    Penalty for undesirable ranges.
    Specific rewards for fine-tuned output ranges.
    Penalty for large deviations.

## Slide 11
RESULTS
I: Conventional PID Tuning
II: RL-Tuned PID

## Slide 12
I: CONVENTIONAL PID TUNING

## Slide 13
II: RL-TUNED PID
Trail: 18

## Slide 14
II: RL-TUNED PID
Trail: 23

## Slide 15
COMPARISON
  Comparison Points:
    Overshoot
    Settling time
    Adaptability
  TD3's Advantages in Dynamic Environments:
    Reduced Overestimation Bias
    Stable Policy Updates
    Smooth Control

## Slide 16
COMPARISON
Conventional PID Controller
RL-Tunned PID Controller
Example
Simscape
Model

## Slide 17
CONCLUSION

## Slide 18
REFERENCES
  "Tuning of PID Controllers Using Reinforcement Learning for Nonlinear Systems Control” - Gheorghe Bujgoi and Dorin Sendrescu
  Simscape Model From Matlab’s Community File Exchange - Link
  MATLAB and Simulink documentation
  Reinforcement Learning Onramp